## Slide 1: Introduction to EEG Processing: Part II
Sarah Sheldon

## Slide 2: Matlab Code on Github: https://github.com/ssheldo/EEG_process_talk
Practice_EEG_Analysis.m demonstrates principles using functions created for processing and analysis (functions found in Kyle_EEG_analysis folder)
outline.m has signal processing examples and demonstrations of principles

## Slide 3
Convert to frequency domain
  Wavelet decomposition
  Wigner distribution
  Fourier transform
How do we describe time varying signals?
Notes: What does stationary mean – statistics are invariant over time.
- how do we analyze it?

## Slide 4: Time-Frequency Analysis
We model our signal as a linear combination of sine waves

## Slide 5: Think of music…
Phase
Amplitude
Frequency

## Slide 6
wikipedia
First 4 Fourier components for the square wave function:
Amplitude: how big is circle
Phase: offset in position on circle
Time domain signal and its frequency spectrum

## Slide 7
FFT: IFFT:
Where is sampled signal obtained from and represent its frequency components. To get a more intuitive idea of what the frequency response represents, consider the system below: Frequency response
http://www.jezzamon.com/fourier/index.html
https://betterexplained.com/articles/an-interactive-guide-to-the-fourier-transform/
Good Interactive Introductions to FFT:

## Slide 8: Fourier Analysis
Any waveform is equivalent to the sum of a set of sine waves of different frequencies, amplitudes and phases
  Time domain: Amplitude as a function of time
  Frequency domain: Amplitude and phase as a function of frequency
Fourier transform converts time domain to frequency domain
Inverse Fourier transform converts frequency domain to time domain
Fourier Transform
Inverse Fourier Transform
Time Domain
Frequency Domain
Amplitude (or Power)
(Phase, too!)
Notes: © S. J. Luck. All Rights Reserved. May be used for nonprofit educational purposes if this copyright notice is included. Permission must be obtained from the copyright holder(s) for any other use.

## Slide 9: Fourier Analysis
Time
Frequency
Amplitude
Amplitude
Square wave at F Hz
Fourier transform of square wave at F Hz
+ 9F + 11F + 13F …

## Slide 10: Phase and the “Imaginary” Component
If you add a sine wave and a cosine wave of the same frequency, you get a sinusoid of the same frequency but a different amplitude and phase
Two different ways to characterize a sinusoid of a given frequency:
Phase and Amplitude
Sine Component and Cosine Component
Amplitude = sqrt(sine2 + cosine2)
Phase = arctan(cosine/sine)

## Slide 11: Phase and the “Imaginary” Component
If you add a sine wave and a cosine wave of the same frequency, you get a sinusoid of the same frequency but a different amplitude and phase
Two different ways to characterize a sinusoid of a given frequency:
Phase and Amplitude
Sine Component and Cosine Component
Amplitude = sqrt(sine2 + cosine2)
Phase = arctan(cosine/sine)

## Slide 12
FFT: IFFT:
Where is sampled signal obtained from and represent its frequency components. To get a more intuitive idea of what the frequency response represents, consider the system below: Frequency response
Y = fft(X,n) returns the n-point DFT.
fft(X) is equivalent to fft(X, n) where n is the size of X in the first non-singleton dimension. If the length of X is less than n, X is padded with trailing zeros to length n. If the length of X is greater than n, the sequence X is truncated. When X is a matrix, the length of the columns are adjusted in the same manner.
y = ifft(X,n) returns the n-point inverse DFT of vector X.
Time domain signal and its frequency spectrum

## Slide 13
Convert to frequency domain
  Wavelet decomposition
  Wigner distribution
  Fourier transform
How do we describe time varying signals?
Notes: What does stationary mean – statistics are invariant over time.
- how do we analyze it?

## Slide 14: FFT and IFFT examples
F1=20;
F2=100;
Fs = 1000; % Sampling frequency
Ts = 1/Fs; % Sampling time
t=0:Ts:.3;
x=sin(2*pi*F1*t)+sin(2*pi*F2*t);
L=numel(x);
Notes: First, lets make a signal that is the sum of two sinusoids

## Slide 15: FFT and IFFT examples
L=301 number of samples.
64-point fft 301-point fft 512-point fft
(Truncated) (N=L) (Zero padded)
Higher variance in FFT peaks
Partial reconstruction in t
Sharp FFT peaks
Full reconstruction in t
FFT is ‘noisy’
iFFT has zeros

## Slide 16: FFT and IFFT examples
F1=20;
F2=100;
Fs = 1000; % Sampling frequency
Ts = 1/Fs; % Sampling time
t=0:Ts:.3;
x=sin(2*pi*F1*t)+sin(2*pi*F2*t);
NFFT = pow2(nextpow2(L));
% Signal plus Zero-Mean Random Noise
noisy_x = x+.5*randn(1,nemel(x));
plot(t,noisy_x,'.-');
fft_noisy_x = fft(noisy_x,NFFT);
plot(f,2*abs(fft_noisy_x(1:NFFT/2+1)),'r.-')
plot(f,4*p2(1:NFFT/2+1),'g.-')
plot((0:1/(NFFT-1):1)*NFFT*Ts,real(ifft_noisy_x),'k.-')

## Slide 17: FFT and IFFT examples
Try: ex2_FFT_IFFT.m
Step through it
Plot fft_x, why does it look like that?
Plot the amplitude spectrum using abs()
  It is symmetric; so just use the 1st half:
Try: ex2_FFT_IFFTPractice.m
Number samples/sec > nyquist?
Number samples/sec < nyquist?
Number FFT < number samples?
Number of iFFT < number FFT?

## Slide 18: Problem with FFT

## Slide 19: Thank You!
Email me if you have any questions: ssheldon@ualberta.ca

## Slide 20: Fundamental Principle #1
Power at a frequency in a Fourier transform does not mean that an oscillation was present at that frequency
  What the #$%$#&@?!!!
  Then what does power at a frequency mean?
Power at a frequency means that a sine wave at that frequency, when added to other sine waves at other frequencies, can create an equivalent waveform
  It does not mean that the biological signal consists of the sum of these sine waves

## Slide 21: Analogy: Money
A $1 bill is equal in value to 4 quarters
  It is not made of 4 quarters!
  It can be exchanged for 4 quarters
  It can also be exchanged for 9 dimes + 10 pennies

## Slide 22: Time-Frequency Analysis
Each slice is the application of one Gabor function at the specified frequency, with amplitude coded by color
The family of Gabor functions is a Morlet wavelet
Csibra et al. (2000, Science)

## Slide 23: What’s the problem with that?
Frequency changes over time

## Slide 24: What would we want?
 Something that includes a temporal weighting

## Slide 25: What would we want?
 Something that includes a temporal weighting

## Slide 26: What would we want?
 Something that includes a temporal weighting
Morlet wavelet

## Slide 27: What is this talk about?
Frequency information at each point in time is a weighted sum of the frequency information of the instantaneous time AND the neighboring time.
Time-frequency representations retain advantages of both time and frequency domain While making only small sacriﬁces to precision:

## Slide 28: How to make a Morlet wavelet
Instead of using many sine waves with diﬀerent frequencies, time-frequency decomposition uses many wavelets with diﬀerent frequencies.

## Slide 29
http://moargeek.com/2014/07/29/nerd-nerd-nerd-nerd-word/

## Slide 30: Wavelet Convolution as a Bandpass Filter
Remember a convolution is the time-varying mapping between a kernel (here the wavelet) and a signal (EEG).

## Slide 33: Some Basics of Neuroscience

## Slide 34: Some Basics of Neuroscience
Resting membrane potential
  -70 mV on inside of cell
Action potentials
  Triggered when membrane potential goes sufficiently positive
  Starts at axon hillock and travels down axon
  Rarely contributes to scalp EEG
Postsynaptic potentials (PSPs)
  Neurotransmitter binds with receptor, opens ion channels
  Excitatory: Positive charges move into cell
  Inhibitory: Negative charges move into cell
  The origin of most EEG signals

## Slide 35: Some Basics of Neuroscience

## Slide 36: Some Basics of Neuroscience